## Slide 1
Conference Presentation
A Neuromorphic Human Detection System Using Thermal and Event Cameras
for Humanoid Robotics
Authors: Rui Shiota, Abderazek Ben Abdallah, Khanh N. Dang and Zhishang Wang
The School of Computer Science and Engineering, The University of Aizu, Aizu-Wakamatsu 965-8580, Fukushima, Japan
August 14 2026
Notes: Open briefly with the target: an event-driven front end for lightweight activity screening. Avoid claiming that the quantitative accuracy was measured on the FPGA hardware.
[Sources]
- User-provided ICKII.pdf (submitted manuscript)

## Slide 2
Contents
2
01
Introduction
02
Motivation
03
Contribution
04
Method
05
Evaluation
06
Discussion
Notes: I will begin by introducing event-driven perception and the research topic. I will then explain why event counting is useful, define the contribution, describe the method, present the evaluation and preliminary results, and close with the current limitations and next steps.
[Sources]
- User-provided experimental records and submitted paper

## Slide 3
Introduction
3
RESEARCH CONTEXT
Event-driven perception
Physical motion
Scene change
GENX320
Brightness events
Event-rate trace
windows
Motion decision
Motion / no motion
Research topic | Platform | Output
Motion detection | OpenMV + FPGA | Binary output
Current evidence | Recorded traces | Preliminary metrics
Notes: This research examines simple motion detection for embedded systems. A GENX320 event camera reports brightness changes caused by movement. OpenMV counts those events in 20 millisecond windows, and a fixed rule outputs motion or no motion. The current quantitative evidence comes from recorded event-rate data.
[Sources]
- User-provided experimental records and submitted paper

## Slide 4
Motivation
4
WHY COUNT EVENTS
Property | Frame camera | Event camera
Output | Full frames | Brightness changes
Timing | Fixed rate | Asynchronous
Processing | Full-image analysis | Event counting
Event stream
x, y coordinates · polarity · time
windows
Event count
Output
Motion / no motion
Continuous motion check by event counting
Notes: Conventional frame cameras repeatedly capture complete images, including periods with little change. An event camera outputs brightness changes only. Therefore, the system can count events continuously and report motion when the count remains high. A separate recognition method could then run only after motion is detected.
[Sources]
- User-provided experimental records and submitted paper

## Slide 5
Contribution
5
OBJECTIVE
Layer | Content | Evidence | Status
Proposal | Event-rate rule | Algorithm definition | Defined
Evaluation | Basic scenarios | 29,366 windows | Completed
Hardware | UART RX → LED | Basys 3 check | Verified
System | FPGA metrics / power | End-to-end test | Pending
Output
MOTION / NO MOTION
FPGA check
UART reception
Notes: The contribution is a simple motion-detection rule. OpenMV counts events in 20 millisecond windows. A threshold and a consecutive-window filter produce a binary motion signal. Recordings of walking, hand waving, sitting, and an empty scene are used for quantitative evaluation. The FPGA UART path was checked separately, so I do not claim that the reported accuracy was measured on the FPGA.
[Sources]
- User-provided experimental records and submitted paper

## Slide 6
System and Evidence Paths
6
METHOD
GENX320
x, y coordinates
polarity · timestamp
H7 Plus
20 ms event count
UART data
Event count
Motion flag
Basys 3
Threshold · 3 windows
Output
Motion / no motion
Recorded data
Basic scenarios → Metrics
Challenge scenarios → Behavior
Hardware check
UART → FPGA → LED
Offline ≠ FPGA
Notes: This slide separates the processing chain from the two evaluation paths. Each camera event contains x and y coordinates, polarity, and a timestamp. OpenMV aggregates the events every 20 milliseconds. The basic scenarios contain predefined walking, hand-waving, sitting, and empty-scene conditions used to calculate metrics. The challenge scenarios contain entry and exit, a moving chair, and a dropped object; they are used only to inspect detector behavior and are excluded from those metrics. The UART-to-FPGA path was checked separately through reception and output behavior.
[Sources]
- User-provided experimental records and submitted paper

## Slide 7
Detection Rule
7
METHOD
1. Count
20 ms
2. Rate
Events / second
3. Compare
> 10,000/s
4. Confirm
3 windows
Parameter | Value | Role
Window | 20 ms | Count
Threshold | 10,000/s | Decide
Filter | 3 windows | Confirm
Temporal filter
HIGH
HIGH
HIGH
MOTION
3 × 20 ms = 60 ms
Confirmation delay: 60 ms
Notes: The algorithm has four operations. First, count events in each 20 millisecond window. Second, convert that count into an event rate. Third, compare the rate with 10,000 events per second. Finally, require three consecutive high windows. With a 20 millisecond window, the confirmation delay is 60 milliseconds.
[Sources]
- User-provided experimental records and submitted paper

## Slide 8
Evaluation Data
8
EVALUATION
Data | Scenarios | Use
Basic scenarios | Walk · wave · sit–stand · empty | Accuracy / recall / F1
Challenge scenarios | Entry/exit · chair · dropped object | Behavior check
Basic scenarios
20 files · 29,366 windows · metrics
Challenge scenarios
15 files · behavior check only
Notes: The recordings are divided into basic and challenge scenarios. The basic scenarios are walking, hand waving, sitting, and an empty scene. These are used to calculate accuracy, recall, precision, and F1. The challenge scenarios are entry and exit, a moving chair, and a dropped object. These are used to inspect detector behavior and are excluded from the reported metrics. The table therefore defines each name by both its contents and its evaluation role.
[Sources]
- User-provided experimental records and submitted paper

## Slide 9
Evaluation Metrics
9
EVALUATION
Ground truth | Rule output | Count
MOTION | MOTION / NO MOTION | TP / FN
NO MOTION | MOTION / NO MOTION | FP / TN
Labels
MOTION
Walk · wave · sitting–standing
NO MOTION
Empty
(TP + TN) / All
Recall
TP / (TP + FN)
Precision
TP / (TP + FP)
F1
P–R balance
Unit: 20 ms window
Accuracy
Notes: Each 20 millisecond window in the basic scenarios is labeled as motion or no motion. Walking, waving, and sitting windows are labeled as motion. Empty-scene windows are labeled as no motion. The offline replay applies the same fixed threshold and three-window filter. Accuracy summarizes all windows, recall shows how often motion windows are detected, and false positives show motion outputs during the empty-scene condition.
[Sources]
- User-provided experimental records and submitted paper

## Slide 10
Basic Scenario Results
10
RESULTS
Chart: 
| Accuracy | Precision | Recall | F1
Score (%) | 95.52 | 100 | 94.56 | 97.21
Chart: 
| Walking | Hand waving | Sitting-standing | Empty
Recall / accuracy (%) | 99.74 | 98.81 | 82.89 | 100
Overall metrics
Correct decision rate by scenario
Notes: On the basic scenarios, overall accuracy is 95.52 percent, precision is 100 percent, recall is 94.56 percent, and F1 is 97.21 percent. The per-condition chart explains where the errors occur. Walking and hand waving are detected reliably. Sitting is lower at 82.89 percent because event activity decreases during weak or stationary periods. Empty-scene accuracy is 100 percent, meaning zero false-positive windows in that condition.
[Sources]
- User-provided experimental records and submitted paper

## Slide 11
Discussion
11
SCOPE
Current evidence
✓
Basic scenarios
✓
Challenge scenarios
✓
Motion metrics
UART reception
Validation roadmap
1
FPGA trace replay
2
Bit-level agreement
3
Latency + power
4
Event → thermal
Remaining work
FPGA replay · latency · power · sensor integration
Discussion: required capability and deployment context
✓
Notes: The predefined walking, waving, sitting, and empty-scene recordings provide the preliminary numerical result. The entry-and-exit, moving-chair, and dropped-object recordings show detector behavior in additional scenarios, but are not included in the metrics. The UART reception path has also been checked on Basys 3. The next step is to replay labeled traces through the FPGA logic and verify bit-level agreement, then measure latency and power. Sensor integration remains a later extension.
[Sources]
- User-provided experimental records and submitted paper

## Slide 12
References
12
1. Shakir Sumit, D. Rambli, and S. Mirjalili, “Vision-Based Human Detection Techniques: A Descriptive Review,” IEEE Access, 2021. DOI: 10.1109/ACCESS.2021.3063028.
2. T. Kryjak, “Event-Based Vision on FPGAs - a Survey,” in Euromicro Symposium on Digital Systems Design, 2024. DOI: 10.1109/DSD64264.2024.00078.
3. J. Gupta and S. Sharma, “Towards Real Time Hardware Based Human and Object Detection: A Review,” in International Joint Conference on the Analysis of Images, Social Networks and Texts, 2022. DOI: 10.1109/AIST55798.2022.10064933.
4. B. Amirgaliyev, M. Mussabek, T. Rakhimzhanova, and A. Zhumadillayeva, “A Review of Machine Learning and Deep Learning Methods for Person Detection, Tracking and Identification, and Face Recognition with Applications,” Sensors, 2025, 25(5):1410. DOI: 10.3390/s25051410.
5. X. Wang et al., “HARDVS: Revisiting Human Activity Recognition with Dynamic Vision Sensors,” in AAAI Conference on Artificial Intelligence, 2022. DOI: 10.48550/arXiv.2211.09648.
6. X. Lin, M. Liu, and H. Chen, “Spike-HAR++: an energy-efficient and lightweight parallel spiking transformer for event-based human action recognition,” Frontiers in Computational Neuroscience, 2024. DOI: 10.3389/fncom.2024.1508297.
7. L. Li et al., “An Event-tailored State-Space Based Model for Pedestrian Detection,” in ACM Multimedia, 2025. DOI: 10.1145/3746027.3755380.
8. T. Trinh, P. C. Le Thien Vu, and P. T. Bao, “Comparing Mask R-CNN backbone architectures for human detection using thermal imaging,” International Journal of Electrical and Computer Engineering, 2024. DOI: 10.11591/ijece.v14i4.pp3962-3970.
9. R. Elgohary, A. K. Mahmoud, O. Khaled, S. Salah, and M. Badawi, “Enhanced Thermal Human Detection in Military Applications Using Deep Learning,” in 2024 International Telecommunications Conference (ITC-Egypt), 2024. DOI: 10.1109/ITCEgypt61547.2024.10620540.
Notes: The predefined walking, waving, sitting, and empty-scene recordings provide the preliminary numerical result. The entry-and-exit, moving-chair, and dropped-object recordings show detector behavior in additional scenarios, but are not included in the metrics. The UART reception path has also been checked on Basys 3. The next step is to replay labeled traces through the FPGA logic and verify bit-level agreement, then measure latency and power. Sensor integration remains a later extension.
[Sources]
- User-provided experimental records and submitted paper