## Slide 1: SEAL: Fault-Tolerant Neuron Model for Spiking Neural Networks on Unreliable DRAM Systems
Authors: Ryoji Kobayashi12, Ngo-Doanh Nguyen34, and Khanh N. Dang2
1 Graduate School of Engineering, The University of Tokyo, Japan
2 School of Computer Science and Engineering, The University of Aizu, Japan
3 DITEN, University of Genoa, Italy
4 Information Technology Institute, Vietnam National University, Vietnam

## Slide 2: Presentation Outline
Introduction
Proposed Methodology
Evaluation
Conclusion and Future Work
References

## Slide 3: Presentation Outline
Introduction
Proposed Methodology
Evaluation
Conclusion and Future Work
References

## Slide 4: Introduction
AI workloads demand intense memory access
  E.g., GPT-3 has over 100 billion parameters
A. Gholami et al., Micro’24 [1]
Notes: The number of parameters, in turn, memory access, in the AL workloads is ever-increasing
3D DRAM is a promising solution to mitigate the so-called memory wall problem
  High bandwidth & low latency

## Slide 5: Introduction
3D-DRAM provides high-bandwidth & low-latency memory access
  E.g., HBM3 provides up to 0.7TB/s
K. Kim and M. Park, IMW’24 [2]
Notes: The number of parameters, in turn, memory access, in the AL workloads is ever-increasing
3D DRAM is a promising solution to mitigate the so-called memory wall problem
  High bandwidth & low latency

## Slide 6: Motivation & Contribution
High accumulation exacerbates retention failure
  Data collapse in network parameters
    E.g., Bit-flipping in weights
Logic Die
Package Substrate
1st DRAM Die
2nd DRAM Die
3rd DRAM Die
4th DRAM Die
3D DRAM
Temperature
TSVs
0
0
1
0
0
1
1
0
MSB
0
0
0
1
0
0
0
0
0
0
0
1
1
0
0
1
…
0
0
0
0
1
1
1
1
0
0
0
1
0
0
0
1
…
LSB
Retention Failure
Example of Bit-Flipping
Notes: In exchange for high performance of 3D DRAM, heat accumulation leads to an increase in retention failure due to high temperature
  Increase leakage current
  Induce data loss by flipping stored bits
Propose a fault-tolerant spiking neuron called SEAL
SEAL is designed to
  Neutralize retention failure (dominance of 1-to-0 error)
  Minimize HW modification from LIF with an independent peripheral controller

## Slide 7: Motivation & Contribution
High accumulation exacerbates retention failure
  Data collapse in network parameters
    E.g., Bit-flipping in weights
Self-Error-Adaptive LIF (SEAL)
  Neutralize retention failure at runtime
  Minimize modification from LIF neuron
Logic Die
Package Substrate
1st DRAM Die
2nd DRAM Die
3rd DRAM Die
4th DRAM Die
3D DRAM
Temperature
TSVs
0
0
1
0
0
1
1
0
MSB
0
0
0
1
0
0
0
0
0
0
0
1
1
0
0
1
…
0
0
0
0
1
1
1
1
0
0
0
1
0
0
0
1
…
LSB
Retention Failure
Example of Bit-Flipping
Notes: Heat accumulation leads to an increase in retention failure due to high temperature
  Increase leakage current
  Induce data loss by flipping stored bits
Propose a fault-tolerant spiking neuron called SEAL
SEAL is designed to
  Neutralize retention failure (dominance of 1-to-0 error)
  Minimize HW modification from LIF with an independent peripheral controller

## Slide 8: Why SEAL?
Prior works mostly rely on synapse-based fault recovery [3-5]
  Exponential scaling of HW overhead
SEAL is a neuron-based approach
  Linear scaling of HW overhead
Hardware-friendly & network agnostic fault-tolerance mechanism
  With the best error recovery among SOTAs
Notes: Why SEAL?
Prior works mostly rely on synapse-based fault recovery, which is exponential
  Neuron-based approach is preferable as it linearly scales
- Furthermore, SEAL shows the best accuracy improvement among SOTAs (see Evaluation)

## Slide 9: Presentation Outline
Introduction
Proposed Methodology
Evaluation
Conclusion and Future Work
References

## Slide 10: Proposed Methodology
Semantics of retention failure
  Fractional => Decrease
01011001
Fractional
Sign
01010001
10
10110100
Fractional
Sign
10110001
10
Fractional
Notes: Semantics of retention failure vary with the fault position
Fractional part => weight values decrease

## Slide 11: Proposed Methodology
Semantics of retention failure
  Fractional => Decrease
  Sign-bit => Increase
01011001
Fractional
Sign
01010001
10
10110100
Fractional
Sign
10110001
10
Fractional
10110100
Fractional
Sign
00110001
10
Sign-bit
Notes: Sign-bit => weight values increase

## Slide 12: Proposed Methodology
Store with inverted sign-bit
  Fractional => Decrease
  Sign-bit => Decrease
01011001
Fractional
Sign
01010001
10
10110100
Fractional
Sign
10110001
10
Fractional
10110100
00110001
10
Sign-bit
00110100
Fractional
Sign
Inverted
10110001
Inverted
Notes: Inconsistency of semantics can be solved by storing the inverted sign-bit
  Can be easily satisfied with bit-wise inversion
Retention failure consistently corresponds to value decrease

## Slide 13: Proposed Methodology
SEAL is designed to stimulate network activity
  : Sum of incoming spikes at
  : Average weight distortion to neuron
where, such that
LIF equation
Proposed error adaptive term
Correct weight
Affected weight
Notes: SEAL works as an excitatory factor in the network by compensating for the decrease in weight value
Error adaptive term is introduced to LIF equation

## Slide 14: Proposed Methodology
Virtual Synaptic Weight (VSW) to minimize the modification from the LIF neuron
LIF equation
Proposed error adaptive term
Notes: Virtual synaptic weight (VSW) is to minimize LIF modification

## Slide 15: Proposed Methodology
Virtual Synaptic Weight (VSW) to minimize the modification from the LIF neuron
LIF equation
Proposed error adaptive term
LIF equation
Introducing VSW
where,
Notes: Error adaptive term is integrated into the LIF equation
HW modification is minimal

## Slide 16: Proposed Methodology
Illustration of how SEAL works
LIF
01001100
00101110
11010101
00010001
Bit-flipping
0
1
1
0
Input
Output
2
2
2
2
Notes: Example of how SEAL works;
  Architecture of LIF neuron-based network

## Slide 17: Proposed Methodology
Illustration of how SEAL works
LIF
01001100
00101110
11010101
00010001
Bit-flipping
0
1
1
0
Input
= 00110010
Output
= 0.50
2
2
2
2
2
10
x
Virtual Synaptic Weight
00011001
2
“1” (Always-on state)
Correct weight
Affected weight
Notes: Example of how SEAL works;
  Architecture of SEAL neuron-based network
    How D and S are computed
    LIF neuron has an additional synapse with an always-on virtual synaptic weight

## Slide 18: Proposed Methodology
Illustration of how SEAL works
LIF
01001100
00101110
11010101
00010001
Bit-flipping
0
1
1
0
Input
= 00110010
Output
= 0.50
2
2
2
2
2
10
x
Virtual Synaptic Weight
00011001
2
“1” (Always-on state)
Correct weight
Affected weight
Reuse of LIF neuron
Notes: Example of how SEAL works;
  Therefore, SEAL is achieved without major modification from conventional LIF
    Can reuse LIF neuron

## Slide 19: Proposed Methodology
Overview of hardware implementation
Neuron Computing Core
TSV
LIF Array
Memory Interface
VSW Controller
Network Interface
Crossbar
…
Controller
DRAM Dies
Spike Decoder
To Neuron Array
LUT
Index Array
Index #1
Index #2
…
Index #i
Index #N
…
VSW Interface
VSW Controller
Flow Controller
From Network Interface
Notes: Hardware architecture is modeled;
  DRAM dies are stacked on top of the logic die
  Neural computing core (PE) encompasses the LIF array and VSW controller
  VSW controller is composed of two main LUTs
Note: Fundamental concept can be applied to other system architectures (e.g., HBM and planar DRAM)

## Slide 20: Proposed Methodology
Overview of hardware implementation
Spike Decoder
To Neuron Array
LUT
Index Array
Index #1
Index #2
…
Index #i
Index #N
…
VSW Interface
VSW Controller
Flow Controller
From Network Interface
Mux
VSW Interface
Decoder
# Neuron | Index ( bits)
#1 | Index 1
#2 | Index 2
#3 | Index 3
… | …
#(N-1) | Index (B-1)
#N | Index B
# Neuron | 
#1 | Index 1
#2 | Index 2
#3 | Index 3
… | …
#(N-1) | Index (B-1)
#N | Index B
Index | Value ( bits)
1 | Var. 1
2 | Var. 2
3 | Var. 3
… | …
B-1 | Var. (B-1)
B | Var. B
Index | 
1 | Var. 1
2 | Var. 2
3 | Var. 3
… | …
B-1 | Var. (B-1)
B | Var. B
Mux
Decoder
Spike Counter
In-Spike
Spk
Addr
Lyr
Input Decoder
LUT Controller
R/W
Addr
Value
Extractor
Notes: Details of LUTs in the VSW controller;
  One is for the neuron-index table, another is for index-VSW
  VSW interface manages LUT access

## Slide 21: Proposed Methodology
LUT implementation strategy
  Use binning approximation
5.022
4.817
4.251
7.338
4.990
6.174
3.907
………
Exact (16 bits)
Index (3 bits)
ID | Range | Base Val.
0 | 3.51 – 4.00 | 3.51
1 | 4.01 – 4.50 | 4.01
2 | 4.51 – 5.00 | 4.51
3 | 5.01 – 5.50 | 5.01
4 | 5.51 – 6.00 | 5.51
5 | 6.01 – 6.50 | 6.01
6 | 6.51 – 7.00 | 6.51
7 | 7.01 – 7.50 | 7.01
Bin Assignment Table
New
# Neurons
2 (010)
1 (001)
7 (111)
2 (010)
5 (101)
0 (000)
………
3 (011)
5.01
4.51
4.01
7.01
4.51
6.51
3.51
………
Notes: Details of LUT implementation in the VSW controller;
  Storing all VSW values is inefficient
  Binning approximation enables the compression of LUT size and HW overhead

## Slide 22: Proposed Methodology
LUT implementation strategy
  Use binning approximation
5.022
4.817
4.251
7.338
4.990
6.174
3.907
………
Exact (16 bits)
Index (3 bits)
ID | Range | Base Val.
0 | 3.51 – 4.00 | 3.51
1 | 4.01 – 4.50 | 4.01
2 | 4.51 – 5.00 | 4.51
3 | 5.01 – 5.50 | 5.01
4 | 5.51 – 6.00 | 5.51
5 | 6.01 – 6.50 | 6.01
6 | 6.51 – 7.00 | 6.51
7 | 7.01 – 7.50 | 7.01
Bin Assignment Table
New
# Neurons
2 (010)
1 (001)
7 (111)
2 (010)
5 (101)
0 (000)
………
3 (011)
5.01
4.51
4.01
7.01
4.51
6.51
3.51
………
Save overheads

## Slide 23: Presentation Outline
Introduction
Proposed Methodology
Evaluation
Conclusion and Future Work
References

## Slide 24: Evaluation
Accuracy assessment:
  Network architecture and benchmark
    MNIST (MLP), F-MNIST (VGG5), CIFAR-10 (VGG16)
  Insert single-bit faults randomly to trained weights
    1-to-0 bit-flipping @ 100%, 90%, 80% ratio
  Change granularity of binning approximation
Hardware evaluation:
  Logic synthesis with Synopsys Design Compiler
    45nm technology node
  Memory modeling:
    DESTINY[6] tool to model 3D-DRAM with 45nm node
Notes: Evaluation is for two major factors: accuracy and HW overhead
  Accuracy is assessed through software execution by inserting random retention faults
  Hardware overhead is obtained from synthesis tools for the logic part / DESTINY tool for 3D DRAM

## Slide 25: Evaluation
Impact on benchmark accuracy
Notes: SEAL always outperforms LIF neuron
Maximum benefit at 100% ratio
  Substantial reliability benefits under error-biased environments

## Slide 26: Evaluation
Impact on benchmark accuracy
+54.60%
+54.87%
+13.04%
Notes: SEAL always outperforms LIF neuron
Maximum benefit at 100% ratio
  Substantial reliability benefits under error-biased environments

## Slide 27: Evaluation
Characteristics of accuracy
  SEAL can be both excitatory and inhibitory factors
=> Constantly providing better accuracy than the LIF neuron
Notes: SEAL can excite and suppress network activity
SEAL always provides better accuracy than LIF
  Works as a modulator of the network

## Slide 28: Evaluation
Impact of binning approximation
  Depends on network architectures & workloads
Notes: Binning approximation is acceptable depending on the network type and dataset.
For example;
  BIN-16 and -8 show better or equivalent accuracy to baseline
  BIN-4 depends on the network model and benchmark

## Slide 29: Evaluation
Impact of binning approximation
  Depends on network architectures & workloads
Even improve accuracy
Significant drop
Notes: Binning approximation is acceptable depending on the network type and dataset.
For example;
  BIN-16 and -8 show better or equivalent accuracy to baseline
  BIN-4 depends on the network model and benchmark

## Slide 30: Evaluation
Hardware evaluation
  Modest overheads
Notes: Hardware overhead is modest
This is because SEAL overhead is proportional to neuron size rather than the number of synapses, which prior works rely on

## Slide 31: Evaluation
Comparison to prior arts
ICCAD’21 [1]
DAC’22 [2]
TCPMT’24 [3]
Notes: Best accuracy recovery among SOTAs

## Slide 32: Presentation Outline
Introduction
Proposed Methodology
Evaluation
Conclusion and Future Work
References

## Slide 33: Conclusion & Future Works
SEAL neuron compensates for retention failure
Virtual Synaptic Weight (VSW) minimizes the modification from the LIF neuron
  VSW controller is independent of neuron types
Results show enhanced fault-tolerance and reasonable HW overhead
Future works include thermal-aware fault-tolerance based on SEAL
Notes: SEAL is designed to deal with retention failure
VSW concept minimize HW modification from LIF neuron
Results show feasibility and HW efficiency

## Slide 34: Presentation Outline
Introduction
Proposed Methodology
Evaluation
Conclusion and Future Work
References

## Slide 35: References
[1] A. Gholami et al., “AI and Memory Wall,” IEEE Micro, 2024.
[2] K. Kim and M.-j. Park, “Present and Future, Challenges of High Bandwidth Memory (HBM),” in 2024 IEEE International Memory Workshop (IMW). IEEE, 2024, pp. 1–4.
[3] R. V. W. Putra et al., “ReSpawn: Energy-Efficient Fault-Tolerance for Spiking Neural Networks considering Unreliable Memories,” in 2021 IEEE/ACM International Conference on Computer-Aided Design (ICCAD). IEEE, 2021, pp. 1–9.
[4] R. V. W. Putra et al., “SoftSNN: Low-Cost Fault Tolerance for Spiking Neural Network Accelerators under Soft Errors,” in Proceedings of the 59th ACM/IEEE Design Automation Conference, 2022, pp. 151–156.
[5] N.-D. Nguyen et al., “NOMA: A Novel Reliability Improvement Methodology for 3-D IC-based Neuromorphic Systems,” IEEE Transactions on Components, Packaging and Manufacturing Technology, 2024.
[6] M. Poremba et al., “DESTINY: A tool for modeling emerging 3D NVM and eDRAM caches,” in 2015 Design, Automation & Test in Europe Conference & Exhibition (DATE). IEEE, 2015, pp. 1543–1546.

## Slide 36
THANK YOU