## Slide 1: Evolutionary Algorithm for STDP-based Spiking Neural Network Model Compression
Author: Yuga Hanyu*, Zhishang Wang† and Khanh N. Dang†
School of Computer Science and Engineering University of Aizu, Fukushima, Japan E-mail: {*m5291018, †zwang, †khanh}@u-aizu.ac.jp
Date: December 16, 2025

## Slide 2: Outline
Introduction
Proposed Method
Evaluation & Result
Conclusion

## Slide 3: Outline
Introduction
Proposed Method
Evaluation & Result
Conclusion

## Slide 4: Spiking Neural Network
Spiking Neural Networks (SNNs) use spikes to communicate information
Compared to traditional Artificial Neural Networks, SNNs are energy efficient
Fig. 1 Structure of an SNN

## Slide 5: SNN on-chip learning
SNNs are suitable for on-chip learning
On-chip learning devices network size limitations
Compression on number of neurons is necessary for such devices
Original
SNN model
Smaller
SNN model
Compression
Deploy
Fig. 2 Compression of an SNN
Notes: I would like to introduce about my research. My research is about training multiple SNN models then merge them into one model. This way of training offers several benefits such as faster training process and collaborative learning. For example, if we decompose dataset and model into 10 datasets and 10 models, the training process becomes 10 times faster excluding the merging process after that. Also, since we will be working on separate dataset, we can do collaborative learning such as train small models in different places, then merge them to create one model that can perform in every place. My main goal is to propose a model merging method that is both computationally efficient and able to produce high accuracy

## Slide 6: On-Chip Ensemble Learning
Split a dataset, train sub-models, and merge into one model
Fig. 3 Overview of Ensemble Learning [1]

## Slide 7: Limitations
Performance Loss: Increased number of sub-models degrades final accuracy
Limited Compression Metric: Only the redundancy between the neurons were considered
->Not suitable for models with no redundant neurons

## Slide 8: Our contributions
Genetic Algorithm (GA) neuron compression: More robust to the increased number of sub-models
Comprehensive neuron metric: Combination of small test and neuron redundancy metric

## Slide 9: Outline
Introduction
Proposed Method
Evaluation & Result
Conclusion

## Slide 10: Overall Flow
Notes: This is the architecture of each individual SNN model. The number of neurons in each layer is arbitrary. Weights are assigned to each connection between the layers, and the weights between input layer and excitatory layer are learning parameters. First, input spikes gets multiplied by weights and proceeds to excitatory layer. Then, if any of the neurons in excitatory layer emits a spike because of input, that neuron sends inhibitory signal to other neurons through inhibitory layer. This is to prevent several neurons from outputting similar spike patterns, making the learning more diverged.

## Slide 11: Chromosome Network Representation
0 | 1 | 0 | 1
Input Layer
Excitatory Layer
Discard
Neuron
Keep
Neuron
Chromosome: Binary array represents neuron selection
Chromosome
Notes: This is the principle of compressing models. We compress models by removing one of the overlapping neurons. This is because if we have overlapping neurons in the final model, that does not contribute to performance. To compress models without losing performance, we need to remove overlapping neurons. From observing 2D receptive fields of both neurons, we can determine which neurons to remove. However, this is not a practical way with bigger models. We need to come up with an algorithm to perform this automatically.

## Slide 12: GA Neuron Compression Flow
Start
Initialize Population
Elitism & Parent Selection
Crossover
Mutation
Termination
Condition
End
False
True
Compression
Number
SNN Model
Neurons to
remove
Notes: This is the architecture of each individual SNN model. The number of neurons in each layer is arbitrary. Weights are assigned to each connection between the layers, and the weights between input layer and excitatory layer are learning parameters. First, input spikes gets multiplied by weights and proceeds to excitatory layer. Then, if any of the neurons in excitatory layer emits a spike because of input, that neuron sends inhibitory signal to other neurons through inhibitory layer. This is to prevent several neurons from outputting similar spike patterns, making the learning more diverged.

## Slide 13: Initialize Population
Start
Initialize Population
Elitism & Parent Selection
Crossover
Mutation
Termination
Condition
End
False
True
Compression
Number
SNN Model
Neurons to
remove
Notes: This is the architecture of each individual SNN model. The number of neurons in each layer is arbitrary. Weights are assigned to each connection between the layers, and the weights between input layer and excitatory layer are learning parameters. First, input spikes gets multiplied by weights and proceeds to excitatory layer. Then, if any of the neurons in excitatory layer emits a spike because of input, that neuron sends inhibitory signal to other neurons through inhibitory layer. This is to prevent several neurons from outputting similar spike patterns, making the learning more diverged.

## Slide 14: Initialize Population (Cnt.)
0 | 1 | 0 | 1
1 | 1 | 0 | 0
1 | 0 | 0 | 1
Chromosome 1
Chromosome 2
Chromosome 3
0 | 1 | 0 | 1
Population
Neurons before compression: 4
Neuron 1: Discard
Neuron 2: Keep
Neuron 3: Discard
Neuron 4: Keep
Chromosome 1
Notes: This is the system architecture of ensemble learning. Each model trains on different subset of data and merged into one model. In this example, we compress each model by 14 neurons before merge. This is to keep the size of final model not too big. How we can compress without losing performance is the main challenge in ensemble learning.

## Slide 15: Initialize Population (Cnt.)
0 | 1 | 0 | 1
Input Layer
Excitatory Layer
Deactivate
Neuron
Keep
Neuron
Chromosome Evaluation 1: Network Testing
Chromosome 1
Notes: This is the principle of compressing models. We compress models by removing one of the overlapping neurons. This is because if we have overlapping neurons in the final model, that does not contribute to performance. To compress models without losing performance, we need to remove overlapping neurons. From observing 2D receptive fields of both neurons, we can determine which neurons to remove. However, this is not a practical way with bigger models. We need to come up with an algorithm to perform this automatically.

## Slide 16: Initialize Population (Cnt.)
Chromosome Evaluation 2: Redundancy Penalty
0 | 1 | 0 | 1
Chromosome 1
1 | 1 | 0 | 0
Chromosome 2
Chromosome 1 has more redundancy: Subtract penalty from test result
Notes: This is the principle of compressing models. We compress models by removing one of the overlapping neurons. This is because if we have overlapping neurons in the final model, that does not contribute to performance. To compress models without losing performance, we need to remove overlapping neurons. From observing 2D receptive fields of both neurons, we can determine which neurons to remove. However, this is not a practical way with bigger models. We need to come up with an algorithm to perform this automatically.

## Slide 17: Initialize Population (Cnt.)
0 | 1 | 0 | 1
1 | 1 | 0 | 0
1 | 0 | 0 | 1
Chromosome 1
Chromosome 2
Chromosome 3
0.69
0.70
0.72
Generation 1 Complete

## Slide 18: Elitism & Parent Selection
Start
Initialize Population
Elitism & Parent Selection
Crossover
Mutation
Termination
Condition
End
False
True
Compression
Number
SNN Model
Neurons to
remove
Notes: This is the architecture of each individual SNN model. The number of neurons in each layer is arbitrary. Weights are assigned to each connection between the layers, and the weights between input layer and excitatory layer are learning parameters. First, input spikes gets multiplied by weights and proceeds to excitatory layer. Then, if any of the neurons in excitatory layer emits a spike because of input, that neuron sends inhibitory signal to other neurons through inhibitory layer. This is to prevent several neurons from outputting similar spike patterns, making the learning more diverged.

## Slide 19: Elitism & Parent Selection (Cnt.)
0 | 1 | 0 | 1
1 | 1 | 0 | 0
1 | 0 | 0 | 1
Chromosome 1
Chromosome 2
Chromosome 3
0.69
0.70
0.72
Generation 1
Generation 2
1 | 0 | 0 | 1
Chromosome 3
0.72
Notes: This is the principle of compressing models. We compress models by removing one of the overlapping neurons. This is because if we have overlapping neurons in the final model, that does not contribute to performance. To compress models without losing performance, we need to remove overlapping neurons. From observing 2D receptive fields of both neurons, we can determine which neurons to remove. However, this is not a practical way with bigger models. We need to come up with an algorithm to perform this automatically.

## Slide 20: Elitism & Parent Selection (Cnt.)
0 | 1 | 0 | 1
1 | 1 | 0 | 0
1 | 0 | 0 | 1
Chromosome 1
Chromosome 2
Chromosome 3
0.69
0.70
0.72
Generation 1
Randomly select 2 parents
Parent 1
Parent 2
Notes: This is the principle of compressing models. We compress models by removing one of the overlapping neurons. This is because if we have overlapping neurons in the final model, that does not contribute to performance. To compress models without losing performance, we need to remove overlapping neurons. From observing 2D receptive fields of both neurons, we can determine which neurons to remove. However, this is not a practical way with bigger models. We need to come up with an algorithm to perform this automatically.

## Slide 21: Crossover
Start
Initialize Population
Elitism & Parent Selection
Crossover
Mutation
Termination
Condition
End
False
True
Compression
Number
SNN Model
Neurons to
remove
Notes: This is the architecture of each individual SNN model. The number of neurons in each layer is arbitrary. Weights are assigned to each connection between the layers, and the weights between input layer and excitatory layer are learning parameters. First, input spikes gets multiplied by weights and proceeds to excitatory layer. Then, if any of the neurons in excitatory layer emits a spike because of input, that neuron sends inhibitory signal to other neurons through inhibitory layer. This is to prevent several neurons from outputting similar spike patterns, making the learning more diverged.

## Slide 22: Crossover (Cnt.)
0 | 1 | 0 | 1
1 | 0 | 0 | 1
Chromosome 1
(Parent 1)
Chromosome 3
(Parent 2)
1 | 1 | 0 | 1
Child 1
0 | 0 | 0 | 1
Child 2
Crossover Point 1
Crossover Point 2
Notes: This is the principle of compressing models. We compress models by removing one of the overlapping neurons. This is because if we have overlapping neurons in the final model, that does not contribute to performance. To compress models without losing performance, we need to remove overlapping neurons. From observing 2D receptive fields of both neurons, we can determine which neurons to remove. However, this is not a practical way with bigger models. We need to come up with an algorithm to perform this automatically.

## Slide 23: Mutation
Start
Initialize Population
Elitism & Parent Selection
Crossover
Mutation
Termination
Condition
End
False
True
Compression
Number
SNN Model
Neurons to
remove
Notes: This is the architecture of each individual SNN model. The number of neurons in each layer is arbitrary. Weights are assigned to each connection between the layers, and the weights between input layer and excitatory layer are learning parameters. First, input spikes gets multiplied by weights and proceeds to excitatory layer. Then, if any of the neurons in excitatory layer emits a spike because of input, that neuron sends inhibitory signal to other neurons through inhibitory layer. This is to prevent several neurons from outputting similar spike patterns, making the learning more diverged.

## Slide 24: Mutation (Cnt.)
Mutation: Chromosome correction & Swap mutation
1 | 1 | 0 | 1
Child 1
Randomly flip 1s
If summation > target (2)
0 | 0 | 0 | 1
Child 2
Randomly flip 0s
If summation < target (2)
0 | 1 | 0 | 1
1 | 0 | 0 | 1
Child 1
Child 2
Randomly swap positions
Randomly swap positions
Notes: This is the principle of compressing models. We compress models by removing one of the overlapping neurons. This is because if we have overlapping neurons in the final model, that does not contribute to performance. To compress models without losing performance, we need to remove overlapping neurons. From observing 2D receptive fields of both neurons, we can determine which neurons to remove. However, this is not a practical way with bigger models. We need to come up with an algorithm to perform this automatically.

## Slide 25: Mutation (Cnt.)
Generation 2
1 | 0 | 0 | 1
Chromosome 3
1 | 1 | 0 | 0
Child 1
1 | 0 | 1 | 0
Child 2
Notes: This is the principle of compressing models. We compress models by removing one of the overlapping neurons. This is because if we have overlapping neurons in the final model, that does not contribute to performance. To compress models without losing performance, we need to remove overlapping neurons. From observing 2D receptive fields of both neurons, we can determine which neurons to remove. However, this is not a practical way with bigger models. We need to come up with an algorithm to perform this automatically.

## Slide 26: Outline
Introduction
Proposed Method
Evaluation & Result
Conclusion

## Slide 27: Evaluation & Result
Setup:
  Machine: core i7-13700K, Nvidia RTX4070
Model:
  Learning Model: pre-and-post-synaptic STDP
  Programming and Library: Python, BindsNet [2]
  5 sub-models, 100 neurons each, merged into a 300 model
  (200 neurons compressed)
  2 sub-models, 250 neurons each, merged into a 300 model
  (200 neurons compressed)
Criterion:
  Classification Accuracy
  Processing Speed of Compression

## Slide 28: GA vs Similarity (Centralized & Ensemble)
Learning Method | Compression Case | Compression Method | Training Time | Compression Time | Accuracy
Centralized | 300 | No compression [2]. | 80.02 minutes | N/A | 88.87%
Ensemble | 5×100-200 | Similarity (Manhattan Dist.) [1] | 15.72 minutes | 2.5 seconds | 85.42%
 |  | Our Genetic Algorithm | 15.72 minutes | 78.3 minutes | 88.46%
Ensemble | 2×250-200 | Similarity (MSE) [1] | 39.5 minutes | 5.9 seconds | 89.28%
 |  | Our Genetic Algorithm | 39.5 minutes | 77.5 minutes | 90.45%

## Slide 29: GA vs Similarity (Single Model)
Compression Case | Compression Method | Compression Time | Accuracy
150-50 | Similarity (MSE) [1] | 0.4 seconds | 84.03%
 | Our Genetic Algorithm | 46.8 minutes | 85.28%
300-100 | Similarity (Cosine Similarity) [1] | 1.8 seconds | 87.97%
 | Our Genetic Algorithm | 52.4 minutes | 88.67%
500-200 | Similarity (Manhattan Dist.) [1] | 4.1 seconds | 90.55%
 | Our Genetic Algorithm | 60.9 minutes | 90.96%

## Slide 30: Outline
Introduction
Proposed Method
Evaluation & Result
Conclusion

## Slide 31: Conclusion
GA achieves higher accuracy with longer time
GA is more robust to the number of sub-models in EnsembleSTDP [1]
Appropriate application will be on-chip learning & server-side compression

## Slide 32: Reference
[1] H. Yuga and K. N. Dang, “Ensemblestdp: Distributed in-situ spiketiming dependent plasticity learning in spiking neural networks,” in 2024IEEE 17th International Symposium on Embedded Multicore/Many-coreSystems-on-Chip (MCSoC). IEEE, 2024, pp. 434–440.
[2] P. U. Diehl and M. Cook, “Unsupervised learning of digit recognition using spike-timing-dependent plasticity,” Frontiers in computational neuroscience, vol. 9, p. 99, 2015.

## Slide 33: Thank you for your attention!
Notes: Always end with a thank you slide
_ Ask if there is any question