## Slide 1: Implementation and Evaluation of a Lossy Spike Compression Framework for Spiking Neural Networks
Satvik GANESH (s1302003)
Supervisor: Khanh N. Dang
School of Computer Science and Engineering
University of Aizu, Fukushima, Japan
Date: August 10th 2026

## Slide 2: Content
Background
Motivation
Proposed Method
Results
Conclusion

## Slide 3: Content
Background
  Spiking Neural Networks
  LIF Neuron
  Rate Coding
  AER
  Pattern Mining Algorithms
Motivation
Proposed Method
Results
Conclusion

## Slide 4: Spiking Neural Networks (SNNs)
Designed to mimic biological neurons, use spikes to convey information [1]
Output Spikes
j
i
Input Layer
Hidden Layers
Output Layer
Input Spikes
wji
Input
Data
(Eg: Images)
Spike Encoding
Spike Decoding
Output
Data
(Eg: Neuron
Index)
Fig. 1: Structure of SNN
j: Pre-synaptic neuron
i: Post-synaptic neuron
wji : Synaptic weight between i and j
Notes: SNNs are 3rd generation of neural networks.
Designed to mimic biological neurons, use spikes to convey information.
Due to this, promise energy efficiency.
Figure shows how input is converted to spike trains, fed to the network and then the output is obtained.

## Slide 5: Leaky Integrate and Fire (LIF) Neuron
U(t)
Iin
Si
Vthres
t
Vreset
t
t
t
t
Inputs
Dendrites
Neuron
Body
Axon
Output
(a)
(b)
Fig. 2: (a) LIF potential dynamics (b) A typical SNN neuron
LIF equation:
: Time constant
: Membrane potential
: Membrane resistance
: Input current
: Output spike
: Threshold potential
: Reset potential
Notes: LIF combines bio-plausibility with computational efficiency.
Left fig shows the LIF potential dynamics.
Here every input spike results in an increase in potential but the potential leaks over time.
When the threshold is reached, an output spike is released.
Formulized with the given equation.
Right fig shows a typical SNN neuron, input spikes are received at the dendrites and the output spikes are released at the axon.

## Slide 6: Rate Coding
Input = 0
Input = 0.5
Input = 1
Input Data
t
t
t
B(n=1, p=0)
B(n=1, p=0.5)
B(n=1, p=1)
Rate Coding
No. of steps
Input data is repeated for a number of steps
Binomial distribution of input features used to identify the spike
Fig. 3: Rate Coding for SNNs
Notes: Converts input intensity into spiking frequency or firing rate
Pixels intensities are used as input features for spike generation
Black pixel means no spike will be generated
Grey pixel means there is 50% chance of spike generation
White pixel means 100% chance of spike generation

## Slide 7: Address Event Representation
Neuromorphic protocol encoding timing and location of spike events [2]
Only conveys the timing and location of active spikes
1 | 0 | 0 | 1
0 | 0 | 1 | 1
1 | 0 | 1 | 0
0 | 1 | 2 | 3
0
1
2
Neuron
Time Step
Spike Data
0 |  |  | 3
 |  | 2 | 3
0 |  | 2 | 
0 | 1 | 2 | 3
0
1
2
Neuron
Time Step
AER Data
Fig. 4: Spike to AER conversion
Location and timing of active spike is recorded
Notes: The figure shows that only timing and location of active spikes (1) are recorded.

## Slide 8: Pattern Mining Algorithms
Find interesting and relevant patterns in dataset
FP-Growth: Builds an FP-Tree to directly extract frequent patterns [3]
FP-Max: Uses an FP-Tree with pruning to find only maximal frequent patterns [4]

## Slide 9: Content
Background
Motivation
Proposed Method
Results
Conclusion

## Slide 10: Motivation
Rate coding: Simple & noise-resilient, but higher spikes = higher energy & latency
Limits scalability in resource-constrained systems

## Slide 11: Observation during Rate Coding
Fig. 5: Temporal redundancy in spikes of a 784-20-10 SNN trained via BPTT on MNIST.
Neurons fire in groups at the same timestep (Fig. 5)
Highly similar spike patterns observed at timesteps 4, 9, 18 in hidden layer
~30.50% spike similarity (Jaccard), so moderate–high temporal redundancy

## Slide 12: Our Contributions
Frequent Spike Pattern Compression (FSPC): A framework for compressing co-firing neuron activity in SNNs [5]
Leverages pattern mining algorithms to identify neuron sets that frequently fire together
Merges these co-firing sets to reduce overall spike data size

## Slide 13: Content
Background
Motivation
Proposed Method
  Pattern Finding Phase
  Compression Phase
Results
Conclusion

## Slide 14: Proposed Method Overview
Pattern Finding Phase
Extract spike tensor from layer ln
Compression Phase
Encode spike tensor to AER
Pattern Mining Function extracts FSPs
Find FSPs in AER data
Compress FSPs with Symbols
PMT
Decompress symbols with FSPs
No. of FSPs
Symbols
Symbols
Decode AER to spike tensor
Send spike tensor to layer ln+1
(1)
(2)
Key Steps:
Pattern Finding Phase
Compression Phase
Fig. 6: FSPC Framework
Notes: Figure shows the overall framework of FSPC

## Slide 15: Important Terms
Frequent Spike Pattern (FSP): Set of neurons firing simultaneously at same timestep
Pattern Match Threshold (PMT): Value (0–1) defining the minimum proportion of FSP neurons that must appear in AER data for a valid match
The required number of FSP neurons in the AER data is:
Nrequired = ⌈PMT × |FSP Set|⌉
|FSP Set| = number of neurons in FSP set
⌈⌉ = ceiling function

## Slide 16: Location of FSPC in SNN
Layer In+1
Layer
In
Input
Layer
Output
Layer
Fig. 7: Location of FSPC in SNN
FSPC

## Slide 17: (1) Pattern Finding Phase
Extract spike tensor from layer ln and encode it to AER
1 | 0 | 1 | 0 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 0 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0
Neuron Index
Time Step
Spike Data
0 |  | 2 |  |  | 5 | 6 | 
0 | 1 |  |  | 4 |  |  | 7
 | 1 | 2 |  |  | 5 | 6 | 
0 |  | 2 |  |  | 5 | 6 | 
0 | 1 |  |  | 4 |  | 6 | 
0 |  | 2 |  |  | 5 | 6 | 7
0 |  | 2 |  |  | 5 | 6 | 
0 |  | 2 |  | 4 | 5 |  | 
Encode to AER Data
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0
1
2
3
4
5
6
7
Convert to AER format
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0
1
2
3
4
5
6
7

## Slide 18: (1) Pattern Finding Phase
0 |  | 2 |  |  | 5 | 6 | 
0 | 1 |  |  | 4 |  |  | 7
 | 1 | 2 |  |  | 5 | 6 | 
0 |  | 2 |  |  | 5 | 6 | 
0 | 1 |  |  | 4 |  | 6 | 
0 |  | 2 |  |  | 5 | 6 | 7
0 |  | 2 |  |  | 5 | 6 | 
0 |  | 2 |  | 4 | 5 |  | 
Extract FSPs using Pattern Mining Algorithms and assign them to symbols
Encoded AER Data
Pattern Mining Algorithms extract FSP
α1 = {0, 2, 5, 6}
α2 = {1, 4}
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0
1
2
3
4
5
6
7
FSP = 2
Extracted FSPs are assigned to symbols

## Slide 19: (1) Pattern Finding Phase
0 |  | 2 |  |  | 5 | 6 | 
0 | 1 |  |  | 4 |  |  | 7
 | 1 | 2 |  |  | 5 | 6 | 
0 |  | 2 |  |  | 5 | 6 | 
0 | 1 |  |  | 4 |  | 6 | 
0 |  | 2 |  |  | 5 | 6 | 7
0 |  | 2 |  |  | 5 | 6 | 
0 |  | 2 |  | 4 | 5 |  | 
Find the presence of FSPs in AER data
Encoded AER Data
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0
1
2
3
4
5
6
7
0 |  | 2 |  |  | 5 | 6 | 
0 | 1 |  |  | 4 |  |  | 7
 | 1 | 2 |  |  | 5 | 6 | 
0 |  | 2 |  |  | 5 | 6 | 
0 | 1 |  |  | 4 |  | 6 | 
0 |  | 2 |  |  | 5 | 6 | 7
0 |  | 2 |  |  | 5 | 6 | 
0 |  | 2 |  | 4 | 5 |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0
1
2
3
4
5
6
7
Scanning AER for the extracted FSPs
Find FSPs in AER

## Slide 20: (2) Compression Phase
Compress FSPs with Symbols in AER data
0 |  | 2 |  |  | 5 | 6 | 
0 | 1 |  |  | 4 |  |  | 7
 | 1 | 2 |  |  | 5 | 6 | 
0 |  | 2 |  |  | 5 | 6 | 
0 | 1 |  |  | 4 |  | 6 | 
0 |  | 2 |  |  | 5 | 6 | 7
0 |  | 2 |  |  | 5 | 6 | 
0 |  | 2 |  | 4 | 5 |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0
1
2
3
4
5
6
7
0 |  | 2 |  |  | 5 | 6 | 
0 | 1 |  |  | 4 |  |  | 7
 | 1 | 2 |  |  | 5 | 6 | 
0 |  | 2 |  |  | 5 | 6 | 
0 | 1 |  |  | 4 |  | 6 | 
0 |  | 2 |  |  | 5 | 6 | 7
0 |  | 2 |  |  | 5 | 6 | 
0 |  | 2 |  | 4 | 5 |  | 
FSPs in AER
0 |  |  |  |  |  |  | 7
 | 1 | 2 |  |  | 5 | 6 | 
0 |  |  |  |  |  | 6 | 
 |  |  |  |  |  |  | 7
0 |  | 2 |  | 4 | 5 |  | 
0
1
2
3
4
5
6
7
Compress FSPs to Symbols
α1 | 
 | α2
α1 | 
 | α2
α1 | 
α1 | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Compressed FSPs
Replacing selected FSPs with α1 and α2

## Slide 21: (2) Compression Phase
0 |  |  |  |  |  |  | 7
 | 1 | 2 |  |  | 5 | 6 | 
0 |  |  |  |  |  | 6 | 
 |  |  |  |  |  |  | 7
0 |  | 2 |  | 4 | 5 |  | 
0
1
2
3
4
5
6
7
Compressed Symbols
α1 | 
 | α2
α1 | 
 | α2
α1 | 
α1 | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Compressed FSPs
Decompress Symbols with FSP in AER data
Replacing symbols α1 and α2 with their FSPs
0 |  | 2 |  |  | 5 | 6 | 
0 | 1 |  |  | 4 |  |  | 7
 | 1 | 2 |  |  | 5 | 6 | 
0 |  | 2 |  |  | 5 | 6 | 
0 | 1 |  |  | 4 |  | 6 | 
0 |  | 2 |  |  | 5 | 6 | 7
0 |  | 2 |  |  | 5 | 6 | 
0 |  | 2 |  | 4 | 5 |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0
1
2
3
4
5
6
7
Decompress Symbols to FSPs

## Slide 22: (2) Compression Phase
Decode recovered AER to spike tensor and send to layer ln+1
AER Data
Decode to Spike Data
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0
1
2
3
4
5
6
7
Revert AER data to spike data
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0
1
2
3
4
5
6
7
0 |  | 2 |  |  | 5 | 6 | 
0 | 1 |  |  | 4 |  |  | 7
 | 1 | 2 |  |  | 5 | 6 | 
0 |  | 2 |  |  | 5 | 6 | 
0 | 1 |  |  | 4 |  | 6 | 
0 |  | 2 |  |  | 5 | 6 | 7
0 |  | 2 |  |  | 5 | 6 | 
0 |  | 2 |  | 4 | 5 |  | 
1 | 0 | 1 | 0 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0 | 1 | 1 | 1
1 | 0 | 1 | 0 | 0 | 1 | 1 | 0
1 | 0 | 1 | 0 | 1 | 1 | 0 | 0

## Slide 23: Compression Types
0 |  | 2 |  |  | 5 | 6 | 
0 | 1 |  |  | 4 |  |  | 7
 | 1 | 2 |  |  | 5 | 6 | 
0 |  | 2 |  |  | 5 | 6 | 
0 | 1 |  |  | 4 |  | 6 | 
0 |  | 2 |  |  | 5 | 6 | 7
0 |  | 2 |  |  | 5 | 6 | 
0 |  | 2 |  | 4 | 5 |  | 
Lossless compression
PMT = 1
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0
1
2
3
4
5
6
7
0 |  | 2 |  |  | 5 | 6 | 
0 | 1 |  |  | 4 |  |  | 7
 | 1 | 2 |  |  | 5 | 6 | 
0 |  | 2 |  |  | 5 | 6 | 
0 | 1 |  |  | 4 |  | 6 | 
0 |  | 2 |  |  | 5 | 6 | 7
0 |  | 2 |  |  | 5 | 6 | 
0 |  | 2 |  | 4 | 5 |  | 
0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0
1
2
3
4
5
6
7
PMT = 0.7
Lossy
compression
α1 = {0, 2, 5, 6}
α2 = {1, 4}
Pattern at timestep 2 and 7: ⌈0.7*4⌉ = 3
elements of α1 present
Notes: FSPC supports both lossless and lossy compression, controlled by PMT.
PMT = 1 indicates lossless compression while PMT < 1 means lossy compression.
In PMT = 0.7, the pattern in timesteps 2 and 7 is chosen as ¾ elements of alpha_1 are present.
It should be noted that in lossy compression, the recovered spike data may not be same as the initial one.

## Slide 24: Content
Background
Motivation
Proposed Method
Results
Conclusion

## Slide 25: Evaluation and Result
Model Configuration:
Datasets Used: MNIST, Fashion-MNIST (3000 images out of 10000)
Framework Used: snnTorch
Pattern Mining Algorithms: mlxtend fpmax [6], PAMI’s FP-growth and maxFP-growth [7]
Minimum Support Value: 0.25 (0.35 for four-layer SNN in F-MNIST)
Criteria: Evaluation based on PMT and FSP
Model | Input Neurons (IN) | Hidden Neurons (HN) | Output Neurons (ON)
Three-layer | 784 | 100 | 10
Four-layer | 784 | 100 (HN1), 60 (HN2) | 10

## Slide 26: Evaluation based on FSP
Fig. 8: Evaluation of FSPC between layer HN1–HN2 in a 784-100-60-10 neuron SNN with respect to FSP
(a) MNIST Dataset
(b) F-MNIST Dataset
*PMT = 0.65
0.26% avg. accuracy drop
20.59% max compression
1.16% avg. accuracy drop
31.50% max compression
FP-growth/maxFP-growth: accuracy falling
fpmax: accuracy falling
FP-growth/maxFP-growth: accuracy stabilizes
fpmax: accuracy stabilizes
Notes: In graphs, the left vertical axis is accuracy and right vertical axis is compression.
The horizonal axis shows number of FSPs
Compression increases with FSP in both datasets
Avg. Accuracy either drops or stabilizes

## Slide 27: Evaluation based on PMT
Fig. 9: Evaluation of FSPC between layer HN1–HN2 in a 784-100-60-10 neuron SNN with respect to PMT
(a) MNIST Dataset
(b) F-MNIST Dataset
*FSP = 1
12.59% loss in compression
15.29% loss in compression
Fpmax/FP-growth/maxFP-growth: accuracy increases
Notes: Similar here as well
PMT increase linked with decrease in compression and increase in accuracy

## Slide 28: Content
Background
Motivation
Proposed Method
Results
Conclusion

## Slide 29: Conclusion
Lossy spike compression proposed for SNNs
12–15% spike-data reduction with 1–3% accuracy loss
Can improve simulation efficiency and support adaptive, hardware-aware compression
Future: Develop faster, more scalable algorithms and test on complex models and datasets

## Slide 30: Publication & Code Availability
This work was published at the 2025 IEEE MCSoC Conference under the title “FSPC: A Lossy Spike Compression Through Correlated-AER Merging in Spiking Neural Networks”
Code implementation is available here: https://github.com/klab-aizu/fspc

## Slide 31: References
[1] W. Maass, “Networks of spiking neurons: The third generation of neural network models,” Electron. Colloquium Comput. Complex., vol. TR96, 1996.
[2] M. A. Mahowald, “Vlsi analogs of neuronal visual processing: A synthesis of form and function,” PhD dissertation, California Institute of Technology, Pasadena, CA, USA, May 1992
[3] J. Han et al., “Mining frequent patterns without candidate generation,” in ACM SIGMOD Conference, 2000, pp. 1–12.
[4] G. Grahne and J. Zhu, “High performance mining of maximal frequent itemsets,” in Proceedings of the 6th SIAM International Workshop on High Performance Data Mining, 2003, p. 34.
[5] S. Ganesh, H. Yuga, Z. Wang, and K. N. Dang, “FSPC: A lossy spike compression through correlated-aer merging in spiking neural networks,” in 2025 IEEE 18th International Symposium on Embedded Multicore/Many-core Systems-on-Chip (MCSoC). IEEE, 2025, pp. 386–393.
[6] S. Raschka, “Mlxtend: Providing machine learning and data science utilities and extensions to python’s scientific computing stack,” The Journal of Open Source Software, vol. 3, no. 24, Apr. 2018.
[7] U. K. Rage et al., “PAMI: An open-source python library for pattern mining,” Journal of Machine Learning Research, vol. 25, no. 209, pp.1–6, 2024.

## Slide 32
Thank you for your attention!