## Slide 1: Low-Power Spiking Neural Network with Clock-gating technique
S1290033
Rui Shiota

## Slide 2: Content
Introduction
Methodology
Results
Disucussion
Conclusion
Reference

## Slide 3: Introduction
SNNs and LIF Neuron
Knowledge of Power

## Slide 4: SNNs and LIF Neuron
Spiking Neural Networks (SNNs)
Brain-inspired models
Mimics biological neurons
Communicates and computes using spikes
Leaky Integrate-and-Fire (LIF) neuron
if Σ(inspike[i] * weight[i]) Threshold
outspike = 1
else
outspike =0

## Slide 5: Knowledge of Power
Power = Dynamic Power + Static Power
    Dynamic Power = Internal Power + Switching Power
    Static Power = Leakage Power
      Internal Power: voltage
      Switching Power: switching activity
      Leakage Power: voltage and size of the modules

## Slide 6: Methodology
Procedure
Design of LIF Neuron
Outspike Computation
Clock Gating Overview
Applying Clock Gating

## Slide 7: Procedure
Order | Task
1 | Implementation of conventional LIF neuron
2 | Simulation
3 | Synthesis
4 | Post-synthesis simulation
5 | Power estimation
6 | Same process with clock-gated LIF neuron
7 | Comparing results

## Slide 8: Design of LIF Neuron
Overall architecture of LIF Neuron
Neuron architecture
Implement 3:2 network
Each neurons have one memory
The number of weight is determined by the number of inspike

## Slide 9: Outspike Computation
i: index of inspike and Weight
n: number of bit of them

## Slide 10: Clock Gating Overview
gclk = clk ∧ clken

## Slide 11: Applying Clock Gating
To maintain accuracy,
Reading of weights by first layer neurons ~ output signal computation ➝ clock enable signal is "1"
~ Reading of weights by first layer neurons again ➝ clock enable signal is "0"

## Slide 12: Results
Experimental Information
Simulation of Conventional Network
Simulation of Clock-gated Network
Simulation of Constantly Clock-gated Network
Power Comparison of Conventional and Clock-gated Neuron
Power Comparison of Conventional and Clock-gated Network

## Slide 13: Experimental Information
Experiment
  Coding: Verilog HDL
  ① In neuron unit
  ② In network unit
    Simulation time: 435 ns
    Clock cycle: 10 ns
  Tool: ModelSim (simulation)
  Synopsys Design Complier (synthesis)
  Synopsys PrimeTime (power estimation)

## Slide 14: Simulation of Conventionl Network
Computation is done every time clock rises

## Slide 15: Simulation of Clock-gated Network
Network works at this timing

## Slide 16: Simulation of Constantly Clock-gated Network
Clock enable is always "0"
No computation

## Slide 17: Power Comparison of Conventional and Clock-gated Neuron
Dynamic Power: 26.23%
Static Power: unchanged
Total Power: 21.77%

## Slide 18: Power Comparison of Conventional and Clock-gated Network
Comparison of Conventional and Clock-gated Network
Dynamic Power: 30.23%
Static Power: almost unchanged
Total Power: 24.70%
Comparison of Conventional and Constantly Clock-gated Network
Dynamic Power: 97.53%
Static Power: 2.95%
Total Power: 80.28%

## Slide 19: Discussion
successfully reduced power
Maintaining accuracy
Investigated maximum reduction

## Slide 20: Conclusion
LIF neuron with and without clock gating
Simulation, synthesis and power estimation
Reduction of power consumption
  21.77% in neuron units
  24.70% in network units

## Slide 21: Reference
[1] Prithwineel Paul, Petr Sosik, Lucie Ciencialova, “A survey on learning models of spiking neural membrane systems and spiking neural networks“, arXiv, March 2024.
[2] Wei Fang, Zhaofei Yu, Yanqi Chen, Timothee Masquelier, Tiejun Huang, Yonghong Tian, “Incorporating Learnable Membrane Time Constant to Enhance Learning of Spiking Neural Networks“, arXiv, August 2021.
[3] Xiaoyan Fang, Derong Liu, Shukai Duan, Lidan Wang, “Memristive LIF Spiking Neuron Model and Its Application in Morse Code“, frontiers, April 2022.
[4] Bennie Mols, “Making AI more energy efficient with neuromorphic computing“, CWI, March 2024.
[5] David Patterson, Joseph Gonzalez, Urs H¨olzle, Quoc Le, Chen Liang, Lluis-Miquel Munguia, Daniel Rothchild, David So, Maud Texier, and Jeff Dean, “The Carbon Footprint of Machine Learning Training Will Plateau, Then Shrink“, IEEE, July 2024.
[6] Carole-Jean Wu, Ramya Raghavendra, Udit Gupta, Bilge Acun, Newsha Ardalani, Kiwan Maeng, Gloria Chang, Fiona Aga Behram, James Huang, Charles Bai, Michael Gschwind, Anurag Gupta, Myle Ott, Anastasia Melnikov, Salvatore Candido, David Brooks, Geeta Chauhan, Benjamin Lee,Hsien-HsinS.Lee, BugraAkyildiz, MaximilianBalandat, Joe Spisak,Ravi Jain, MikeRabbat,KimHazelwood, “Sustainable AI: Environmental Implications, Challenges and Opportunities“, arXiv, March 2024.
[7] Nandita Srinivasana, Navamitha.S.Prakasha, Shalakha.Da, Sivaranjani.Da, Swetha Sri Lakshmi.Ga, B.Bala Tripura Sundari, “Power Reduction by Clock Gating Technique“, ScienceDirect, November 2015.
[8] Wenzhe Guo, Mohammed E. Fouda, Ahmed M. Eltawil and Khaled Nabil Salama, “ Neural Coding in Spiking Neural Networks: A Comparative Study for Robust Neuromorphic Systems“, frontiers, March 2021.

## Slide 22
Thank you for your attention!

## Slide 23: Back up slides
You don't present it
If you got questions about it, you can show