## Slide 1: Research Progress Report Seminar Spiking Neural Network with 3-D IC-based Stacking Memory
Ngo-Doanh NGUYEN - m5262108
Supervised by Prof. DANG Nam Khanh
2023-12-01

## Slide 2: Agenda
Motivation
Approach & Methodology
Proposal Hardware Architecture
Results
Conclusion

## Slide 3: Agenda
Motivation
Approach & Methodology
Proposal Hardware Architecture
Results
Conclusion

## Slide 4: Motivation
=> Low-power Spiking Neural Network with 3D-stacking-memory
*J.Hennessy, D. Patterson 2019 CACM
End of Moore's Law
3-D Stacking Arch.
- Reduce Latency
- Reduce Power Consumption
- Reduce Hardware Footprint
Computational Power
for Edge Devices
AI Enabled Devices
- Improve Data Transfer
Efficiency
+ Reduce Latency
+ Reduce Power
High Complexity
for Edge Devices
Spiking Neural Net.
- Lightweight Inference
- Reduce Power Consumption
- Reduce Memory Footprint
- Reduce Hardware Area
*Y. Du. Decentralized Smart IoT. Encyclopedia
10-20 Billion Op.
Weight size > 200MB
*S. H. Tsang. Towards Data Science

## Slide 5: Agenda
Motivation
Approach
Proposal Hardware Architecture
Results
Conclusion

## Slide 6: Approaches (1)
From 2D Architecture to 3D Architecture
  Reduce hardware footprint
  Shorten data movement
  Reduce power delivery
Package Substrate
Logic Die
1st Memory Die
2nd Memory Die
3rd Memory Die
Package Substrate
Logic Die
Mem 1
Mem 2
Mem 0
Processing Elements
n x m
(n+a) x (m+b)
(2n + a) x (2m + b)
2D hardware architecture
3D hardware architecture

## Slide 7: Approaches (2)
Each layer in 3D architecture can have isolated power rails
  Power-gating*, voltage-scaling** differently for each layer
    Reduce supply voltage for low-priority layer or power-gate it
    Maintain supply voltage for high-priority layer
Package Substrate
Logic Die
1st Memory Die
2nd Memory Die
3rd Memory Die
Power management for each layer
Power rails
Power rail
*Power-gate = Remove supply voltage to reduce power consumption
**Voltage-scaling = Reduce supply voltage to reduce power consumption

## Slide 8: Recap: Supply Voltage in Digital Circuits
Normal operation
Undervolting operation
Powergating operation
0
VDD (V)
t(s)
VT=VDD/2
1
Bit
0
Expected Voltage
Real Voltage
0
VDD (V)
t(s)
VT=VDD/2
1
Bit
0
Reduced Voltage
Real Voltage
0
VDD (V)
t(s)
VT=VDD/2
1
Bit
0
Powergated
Real Voltage

## Slide 9: Approaches (3)
Spike Neural Network is spatial and temporal sparse
  Lightweight inference
  Low power delivery
SNN has noise resilience
  Against the affection of power-gate & voltage-scaling
Information
Training
SNN Model
Input Spike
HW
Impl.
Output Spike
Processing
Enc.

## Slide 10: Agenda
Motivation
Approach & Methodology
Proposal Hardware Architecture
Results
Conclusion

## Slide 11: Proposal Hardware Architecture
3D Neuromorphic Computing Core (3D-NCC)
  Split memory into subsets placed in multiple layers
  Power-gate & under-voltage are applied separately to each memory layer => Lower power consumption
  In-situ dynamic quantization for synaptic weights => Maintain accuracy
Address
Decoder
...
Synapse Val.
TSV
TSV
...
x M
1st Memory Die - m0
Mth Memory Die - mM-1
Wi [0:n-1] = 11 1001 ... 1101
Layer
11
100
Weight
Bits
m0
m1
m2
mM-1
...
1
...
1101
3D-NCC Architecture
Bit weight organization

## Slide 12: Weight operation (1)
Operation of 3D-NCC under normal condition
Operation of 3D-NCC with under-volting top layer
Flipped bits
due to under-
volting
Output
stays the
same

## Slide 13: Weight operation (2)
Operation of 3D-NCC under power-gating top layer
Operation of 3D-NCC with both PG & UV
bits are
treated as
zeros
Output
stays the
same

## Slide 14: Agenda
Motivation
Approach & Methodology
Proposal Hardware Architecture
Results
Conclusion

## Slide 15: Accuracy vs. Power (1)
Dataset: MNIST; SNN config. = 784:48:10 (1 3D-NCC)
Power extraction with PrimeTime Synopsys
Lib: NANGATE 45nm + OpenRAM + FreePDK 3D45 TSV
Undervolt each layer (one-by-one) with the same volt.
Accuracy per Volt.
Energy per Volt.
Bit Error Rate per Volt.
reduce ~30% energy
while maintaining
accuracy

## Slide 16: Accuracy vs. Power (2)
Using both power-gating or under-volting for each layer
UV two top layers
PG top layer &
UV second top layer
PG two top layers &
UV two bottom layers
reduce 3x energy
while reducing
~6.5% accuracy

## Slide 17: Comparison
Setup voltage supplies as in case 1, case 2 and case 3
[1]
[2]
[3]
[4]
[5]
~22% accuracy drop in big network

## Slide 18: Agenda
Motivation
Approach & Methodology
Proposal Hardware Architecture
Results
Conclusion

## Slide 19: Conclusion
3D SNN architecture called 3D-NCC
Split memory word into subsets placed in separated layer
  Apply power-gating & voltage-scaling to memory layer(s)
    Reduce power consumption while maintaining accuracy
  In-situ dynamic quantization
UV two top layer reduces 21.62% power consumption with 0.51% accuracy loss
PG two top layer & UV two bottom layers reduce 66.77% power consumption with 6.58% accuracy loss

## Slide 20: Schedule
Submit the draft of thesis
Prepare presentation slides
Submit the final thesis
Thesis presentation
Review & submit the final thesis
Now - 04.12.23
04.12.23 - 26.12.23
04.12.23 - 26.01.24
26.01.24 - 16.02.24
16.02.24 - 22.02.24
- Prepare & submit the draft of the master's thesis
- Prepare the presentation slides based on publication materials
- Polish the draft of master's thesis and submit the final version
- The presentation day
(16.02.24)
- Fix the thesis according the reviews of referees

## Slide 21: References
[1] F. Akopyan et al., “TrueNorth: Design and tool flow of a 65 mW 1 million neuron programmable neurosynaptic chip,” IEEE Trans. Comput. Aided Design Integr. Circuits Syst., vol. 34, no. 10, pp. 1537–1557, Oct. 2015.
[2] M. Davies et al., “Loihi: A neuromorphic manycore processor with on-chip learning,” IEEE Micro, vol. 38, no. 1, pp. 82–99, Jan. 2018.
[3] C. Frenkel, C. Frenkel, M. Lefebvre, J.-D. Legat, and D. Bol, “A 0.086-mm2 12.7-pJ/SOP 64k-synapse 256-neuron online-learning digital spiking neuromorphic processor in 28nm CMOS,” IEEE Trans. Biomed. Circuits Syst., vol. 13, no. 1, pp. 145–158, Feb. 2019.
[4] O. M. Ikechukwu, K. N. Dang, and A. B. Abdallah, “On the design of a fault-tolerant scalable three dimensional NoC-based digital neuromorphic system with on-chip learning,” IEEE Access, vol. 9, pp. 64331–64345, 2021.
[5] M. Karimi, A. S. Monir, R. Mohammadrezaee, and B. Vaisband, “CTT-based scalable neuromorphic architecture,” IEEE J. Emerg. Sel. Topics Circuits Syst., vol. 13, no. 1, pp. 96–107, Mar. 2023.

## Slide 22: Publications
Journal (Published)
  N. -D. Nguyen, A. B. Ahmed, A. B. Abdallah and K. N. Dang, "Power-Aware Neuromorphic Architecture With Partial Voltage Scaling 3-D Stacking Synaptic Memory," in IEEE Transactions on Very Large Scale Integration (VLSI) Systems, doi: 10.1109/TVLSI.2023.3318231.
  N. -D. Nguyen, X. -T. Tran, A. B. Abdallah and K. N. Dang, "An In-Situ Dynamic Quantization With 3D Stacking Synaptic Memory for Power-Aware Neuromorphic Architecture," in IEEE Access, vol. 11, pp. 82377-82389, 2023, doi: 10.1109/ACCESS.2023.3301560.
Conference: (Accepted)
  N. -D. Nguyen and K. N. Dang, “A Novel Yield Improvement Approach for 3D Stacking Neuromorphic Architecture”, 16th IEEE International Symposium on Embedded Multicore /Manycore SoCs (MCSoC-2023), Dec 18th-21th, Singapore, Singapore.

## Slide 23: Thank you for your attention.

## Slide 24: Signal Noise Margin
SNM is to get the Bit Error Rate of memory (SNM<0.1)
6T SRAM (FreePDK NANGATE 45nm)
HSPICE simulation + mathematical computations
Monte Carlo simulation
Signal Noise Margin of 6T SRAM