## Slide 1: A Resilient On-Chip STDP Learning Under Memory Voltage Scaling
Subbaiah Ravi Hariprakash
Supervised by Prof. Khanh N. Dang
m5282026
06/08/2026

## Slide 2: Content
Introduction
Proposed Method
Results
Conclusion

## Slide 3: Content
Introduction
  Energy Consumption
  Types of Learning
  Spiking Neural Networks (SNNs)
  LIF Neuron
  On-Chip STDP Learning
  Overall Architecture
  Voltage effects on DRAM and SNNs
Proposed Method
Results
Conclusion

## Slide 4: Introduction
(a) Predicted power consumption due to AI usage
(b) Energy consumption breakdown of three CNNs on a modern CNN accelerator
Energy consumption due to memory (DRAM) ~50% - 70%
Notes: AI consumes lot of power
Of that memory is 50 % to 70%

## Slide 5: Off-Chip and On-Chip Learning
Raw Data
(e.g Images)
Fixed Model
(a) Off-Chip learning
Neural Network trained
(b) On-Chip learning
Neural network trained locally
High energy efficiency needed for on chip
Notes:   In AI computation, training takes time and energy
  2 types of training
  Off chip: upload to server,
  On chip: no cloud, system learn on its own
  In this research, we want to do on chip
  Fundamental problem is energy,

## Slide 6: Spiking Neural Networks
0
1
2
3
4
5
I
n
p
u
t
S
p
i
k
e
s
…
L
a
b
e
l
C
o
u
n
t
i
n
g
L
a
b
e
l
1
:
2
s
p
i
k
e
s
L
a
b
e
l
2
:
0
s
p
i
k
e
s
L
a
b
e
l
3
:
1
0
s
p
i
k
e
s
…
L
a
b
e
l
N
:
1
s
p
i
k
e
s
Input Spike
L
a
t
e
r
a
l
I
n
h
i
b
i
t
o
r
y
N
-
1
N
-
2
N
-
3
N
-
4
C
l
a
s
s
i
f
i
c
a
t
i
o
n
O
u
t
p
u
t
I
n
p
u
t
s
i
g
n
a
l
Output Spike
Excitatory
A Spiking Neural Network (SNN) topology employing On–Chip Spike-Timing Dependent Plasticity (STDP)
Notes: Fig shows A Spiking Neural Network (SNN) topology employing On–Chip Spike-Timing Dependent Plasticity (STDP)
I/p spikes enter, causes neuron to excite, sends negative signal to other neurons
Classification based on which neuron has most spikes
i/p from rate coding
How does the neuron work? LIF neuron

## Slide 7: Leaky Integrate and Fire (LIF) Neuron
V(t)
(b) LIF Potential dynamics
t
(a) Typical SNN Neuron
LIF equation:
: Time constant
V: Membrane potential
: Resting potential
: Excitatory potential
: Inhibitory potential
, : Dynamic Conductance
: Input current
: Output spike
: Threshold potential
: Reset potential
t
t
t
t
Inputs
Output
Neuron Body
Axon
Dendrites
Notes: Illustration of LIF neuron
Fig a shows typical neuron connection
Fig b shows dynamics of LIF neurons with i/p current and how i/p potential V leak and Vthres

## Slide 8: On-Chip STDP Learning
Equation:
LIF
(a) LIF neuron and spike timings
Notes: This slide shows how On-chip STDP works
Fig a is a single LIF neuron with spike timing tpre and tpost
Fig b and c show 2 cases: tpre before tpost and tpost before tpre
Fig d shows how the weights are updated with the timings

## Slide 9: Overall Architecture
Logic Die
Package Substrate
TSV
TSV
TSV
TSV
.....
3rd Memory Die
1st Memory Die
2nd Memory Die
kth Memory Die
Architecture of proposed system
LIF
Neurons
STDP Learning Controller
STDP-DIP Boot-Time BIST
Our Thesis/Research focus
Part of "Y. Hanyu, R. Kobayashi, S. R. Hariprakash, S. Ganesh, N.-D. Nguyen, D.-A. Nguyen, M. Maatar, A. Ben Abdallah, Z. Wang, and K. N. Dang, 'E3STDP: Energy-Efficient Ensemble Spike-Timing-Dependent Plasticity for Carbon-Aware Neuromorphic Computation.’” IEEE Transactions on Sustainable Computing (under major revision)
Notes: This slide shows our Overall Architecture and where the focus of this research is which is DRAM stacking on top of the logic die
This research is a part of a collaborative research which is under major revision in IEEE Transactions on Sustainable Computing at the moment
Although SNN offers better Energy efficiency, we are still searching for even lower energy numbers. As we mention earlier memory plays a major part, we would like to tackle it in this research

## Slide 10: Undervolting DRAM
Trade-off: Triggers an exponential increase in memory retention errors (up to ~35% BER)
Scaling down supply voltage (1.30V to 1.00V) saves dynamic power quadratically
(c) Graph showing Voltage vs Error obtained from HSPICE simulations using a 45 nm CMOS technology
Notes: One of the solution is Undervolting the memory or reducing the supply voltage
There are drawbacks of undervolting DRAM cell,
Fig a shows incoming leakage
Fig b shows outgoing leakage
To understand more we ran a single DRAM cell HSPICE sim with Monte Carlo Sim and 45nm and obtained graph c
In summary we can scale down power consumption dramatically, however memory retention error increases

## Slide 11: Memory Fault Behaviours Under Undervolting
Soft Errors (Bit-Flips):
  Temporary data glitches
Permanent Errors:
  Caused by manufacturing defects
  Exposed due to aggressive undervolting
  This research focuses on Stuck-at Faults
  Weak cells leak charge, permanently locks physical cell to ground (0) or supply voltage (1)
0
1
(a) Normal bit update
0
1
(b) Bit flip
0
1
(c) Bit stuck-at
Notes: Now we see the effects
Soft errors are Temporary data glitches
Permanent errors

## Slide 12: Impact of SA0 vs SA1 Faults
Stuck-at-0 (SA0):
  Weight locked to minimum conductance
  Easily absorbed, accuracy remains stable (>90%).
Stuck-at-1 (SA1):
  Weight locked to maximum conductance
  Neuron fires continuously
  Suppresses all healthy neurons
  Accuracy collapses from 92.0% to 10.9%*
(e) Normal Field
(f) SA0 Field
(g) SA1 Field
*Data obtained from STDP Learning model with 784 weights per 1000 neuron network, MNIST dataset
Notes: We would like to see the impact of SA0 and SA1 on On-chip STDP learning
LHS is how we insert fault.
To have the most impact we insert in the MSB
Other bit indices have lower impact
B/w SA0 and SA1, we observe SA0 has almost no impact, and SA1 collapses STDP learning
Accuracy collapses from 92.0% to 10.9% *Data obtained from STDP Learning model with 784 weights per 1000 neuron network, MNIST dataset
Fig e f g show receptive fields of same neuron under 3 cases: Normal, SA0, SA1

## Slide 13: Related Work
Error Correction Codes:
  Requires 12.5% to 37.5% storage area overhead
  Encoding/decoding negates 40% energy saved
Checkpointing:
  Milliseconds of latency per save
  Incurs >100% to 200% power overhead
Inference Mitigations:
  Protects only pre-trained networks
  Energy overhead 15% to 30%
Memory Checking:
  Can check for MSB and LSB
  Energy overhead 30% to 50%
Unsuitable for On-chip STDP learning
Notes: How others have approached this problem
(Read first bullet point for all methods)
However, the common problem is overhead in power and energy which makes them unsuitable of On-chip STDP learning

## Slide 14: Problem Statement and Contributions
Problem:
  Near-threshold undervolting to lower consumption
  Low voltages cause stuck-faults and flip bits
  SA1 destroys STDP learning
Contributions:
  Characterized SA1 behavior under eDRAM voltage scaling
  Proposed STDP-DIP to identify, isolate and prune faulty neurons

## Slide 15: Content
Introduction
Proposed Method
Results
Conclusion

## Slide 16: STDP-DIP: Diagnostic Isolation Pruning
Phase 1: Detects SA1 at MSB in the weight matrix
Phase 2: Faulty neuron is structurally severed
Phase 3: Output of faulty neuron unlabeled

## Slide 17: STDP-DIP: Proposal Overview
0
1
2
3
4
5
I
n
p
u
t
S
p
i
k
e
s
…
L
a
b
e
l
C
o
u
n
t
i
n
g
L
a
b
e
l
1
:
2
s
p
i
k
e
s
L
a
b
e
l
2
:
0
s
p
i
k
e
s
L
a
b
e
l
3
:
1
0
s
p
i
k
e
s
…
L
a
b
e
l
N
:
1
s
p
i
k
e
s
Input Spike
Lateral Inhibition
N
-
1
N
-
2
N
-
3
N
-
4
C
l
a
s
s
i
f
i
c
a
t
i
o
n
O
u
t
p
u
t
I
n
p
u
t
s
i
g
n
a
l
Output Spike
Excitatory
DIP: Inhibitory connection severed
Stuck at 1
Overview of STDP network and STDP-DIP
Notes: This slide shows an overview of STDP –DIP
The red neuron 1 has SA1 fault, out principle is to detect and cut it off

## Slide 18: STDP-DIP: Detection
MSB faults observed to cause most impact
Synaptic weights of neurons checked for Stuck-at-1 MSBs
Another way is to detect hyperactive (fires continuously) neuron
Why?
  Memory check exists but needs 30% to 50% more energy
  ECC negates 40% energy saved
(a) Bit values of synaptic weights of healthy neuron
(b) Bit values of synaptic weights of SA1 neuron
Bit permanently Stuck at 1
1
1
1
0
1
1
0
0
MSB
LSB
0
1
1
0
1
1
0
0
MSB
LSB
Notes: As previously mentioned, SA1 at MSB cause the most impact
Our principle is to check stuck at 1 MSB
(Just read)
In a healthy SNN, starting synaptic weights (𝑊_0) are generated from a random distribution tightly bounded at low conductance values (e.g., 0.01 to 0.20)
SA1 fault physically shorts the memory cell to 𝑉_𝐷𝐷 forcing the 8-bit weight register to all ones (11111111 or 〖1.0〗_𝑚𝑎𝑥)
Any synapse reading exactly maximum conductance (1.0) at boot-time is mathematically impossible for a healthy initialization and is deterministically flagged as a physical short.

## Slide 19: STDP-DIP: Algorithm (1)
Brief lateral inhibition triggered by each spike
Healthy competition and diverse feature learning
4
Input Spikes
Label Counting (Output)
Input Spike
Lateral Inhibition
Input Signal
Output Spike
Excitatory
1
0
2
Excitatory Layer
: Digit 4
: Digit 2
: Digit 7
Normal STDP Operation
Notes: This slide shows a simplified visualisation with only 3 neurons for ease of understanding
Here after receiving input spike, this neuron can fire and exhibits Lateral Inhibition to other neurons

## Slide 20: STDP-DIP: Algorithm (2)
Faulty neuron fires continuously
Runaway lateral inhibition, paralyzes neurons, stops learning
4
Input Spike
Lateral Inhibition
1
0
2
Excitatory Layer
(a) Uncorrected SA1 Fault
Healthy neurons paralyzed by continuous lateral inhibition
Stuck at 1
Input Spikes
Input Signal
Label Counting (Output)
: 0 Spikes
: Many Spikes
: 0 Spikes
Time t
Neuron Index
2
1
0
(b) Spike timing
Notes: Here is the same visualisation where Neuron 1 has SA1
As mentioned before, it becomes hyperactive
(Just read)

## Slide 21: STDP-DIP: Algorithm (3)
Detect faulty neuron
Faulty neuron connection severed
Healthy STDP spiking restored
Input Spikes
Input Signal
4
Input Spike
SA1 Detected: Inhibition Severed
1
0
2
Excitatory Layer
Corrected using STDP-DIP
Normal Lateral Inhibition
Output Spike
Label Counting (Output)
: Digit 4
: (Masked)
: Digit 7
Notes: This slide shows how we fixed it
We detect the faulty neuron

## Slide 22: Spike Behaviour Restoration
Notes: LHS is spike timing with SA1 at Neuron 4
RHS is by doing STDP-DIP to restore other neurons

## Slide 23: Content
Introduction
Proposed Method
Results
Conclusion

## Slide 24: Simulation Setup
Environment: Python, PyTorch, BindsNET, Ran with 3 different seeds
Hardware Model: 45nm PTM CMOS eDRAM, Monte Carlo simulation done with HSPICE (100000 trials per case)
Network: LIF-STDP model
Dataset: Poisson-encoded MNIST

## Slide 25: Fault Insertion
…
…
…
…
…
…
Faulty neurons chosen randomly
MSB of weights flipped manually
Simulates SA1 fault
: Number of Neurons (1000)
: Number of weights (784)
1
1
1
0
1
1
0
0

## Slide 26: Results: 400 Neurons
(a) Plot between accuracy before and after correction for 5 SA1 neurons in a 400 neuron network
(b) Plot between accuracy before and after correction for 15 SA1 neurons in a 400 neuron network
Bit Error Rate (BER)
Test Accuracy (%)
Bit Error Rate (BER)
Accuracy improved by 73% - 79%
Notes: 400 neuron with diff BER, in summary accuracy improved by …

## Slide 27: Results: 1000 Neurons
(a) Plot between accuracy before and after correction for 5 SA1 neurons in a 1000 neuron network
(b) Plot between accuracy before and after correction for 15 SA1 neurons In a 1000 neuron network
Bit Error Rate (BER)
Bit Error Rate (BER)
Test Accuracy (%)
Accuracy improved by 71% - 81%
Notes: 1000 neuron with diff BER, in summary accuracy improved by …

## Slide 28: Results: All cases
Notes: This slide shows all cases
In summary we can restore to original accuracy

## Slide 29: Results: Training With Fault Correction
(b) Network trained using proposed STDP-DIP framework
Faulty neuron isolated
(a) Network trained with SA1 fault and no correction

## Slide 30: Results: Energy Saved
Relative Energy reduction
: Undervolted potential
: Nominal potential
40.83% reduction by scaling supply voltage down to 1.00V
20.4% to 30.6% total energy reduction
  Assumption: Memory energy 50% to 75%
Notes: We have shown that we can restore the overall accuracy
One question is how much energy can be saved with undervolting
This equation shows the relative energy reduction
(Just read)

## Slide 31: Content
Introduction
Proposed Method
Results
Conclusion

## Slide 32: Conclusion
Identified impact of SA1 memory faults on On-Chip STDP learning
Developed STDP-DIP to improve accuracy
  Restored >91% accuracy while saving 30.6% system energy
Future Work
  Explore different learning approach
  Explore mixed-fault scenarios (SA0 + SA1)

## Slide 33: References
[1] International Energy Agency (IEA), "Global Data Centre Electricity Consumption Report," Paris, France, Tech. Rep., 2025.
[2] Y.-H. Chen, T. Krishna, J. S. Emer, and V. Sze, "Eyeriss: An Energy-Efficient Reconfigurable Accelerator for Deep Convolutional Neural Networks," IEEE Journal of Solid-State Circuits, vol. 52, no. 1, pp. 127–138, Jan. 2017, doi: 10.1109/JSSC.2016.2616357.
[3] P. J. Nair, D. A. Roberts, and M. K. Qureshi, "Faulty: A Reliable Data-Bus Architecture for Low-Voltage DRAMs," 2013 IEEE 31st International Conference on Computer Design (ICCD), Asheville, NC, USA, 2013, pp. 432–439, doi: 10.1109/ICCD.2013.6657078.
[4] H. Hassan, L. Orosa, R. Ausavarungnirun, and O. Mutlu, "SoftMC: A Flexible and Open-Source FPGA-Based Memory Controller for Memory Characterization and Testing," IEEE Transactions on Computers, vol. 72, no. 4, pp. 1020–1034, Apr. 2023, doi: 10.1109/TC.2022.3198765.
[5] W. W. Hargrove and J. Pickering, "Pseudoreplication: a review of its history and a recommendation for its avoidance," Conservation Biology, vol. 3, no. 4, pp. 389–397, Dec. 1989, doi: 10.1111/j.1523-1739.1989.tb00245.x.
[6] R. V. W. Putra, M. A. Hanif, and M. Shafique, "DRiP: Dynamic Refresh and Precision Scaling for Approximate DRAM in DNN Accelerators," 2021 IEEE/ACM International Conference On Computer Aided Design (ICCAD), Munich, Germany, 2021, pp. 1–9, doi: 10.1109/ICCAD51581.2021.9643534.
[7] R. Kobayashi and K. N. Dang, "An Efficient Hardware Implementation of Spiking Neural Network Using Approximate Izhikevich Neuron," 2024 9th International Conference on Integrated Circuits, Design, and Verification (ICDV), Hanoi, Vietnam, 2024, pp. 13-18, doi: 10.1109/ICDV61346.2024.10616602.
[8] Ryoji Kobayashi, Ngo-Doanh Nguyen, Nguyen Anh Vu Doan and Khanh N. Dang, '’Energy-Efficient Spiking Neural Networks Using Approximate Neuron Circuits and 3D Stacking Memory’‘, 2024 IEEE 17th International Symposium on Embedded Multicore/Many-core Systems-on-Chip (MCSoC), Dec. 16-19, 2024.

## Slide 34: References
[9] Du, Y. Decentralized Smart IoT. Encyclopedia. Available online: https://encyclopedia.pub/entry/8977 (accessed on 22 November 2022).
[10] S. H. Tsang, https://towardsdatascience.com//review-refinenet-multi-path-refinement-network-semantic-segmentation
[11] John L. Hennessy, David A. Patterson, A New Golden Age for Computer Architecture, Communications of the ACM, February 2019, Vol. 62 No. 2, Pages 48-60, 10.1145/3282307
[12] J. Wuu et al., "3D V-Cache: the Implementation of a Hybrid-Bonded 64MB Stacked Cache for a 7nm x86-64 CPU," 2022 IEEE International Solid-State Circuits Conference (ISSCC), San Francisco, CA, USA, 2022, pp. 428-429, doi: 10.1109/ISSCC42614.2022.9731565.
[13] H. Songara and A. Deshwal, "Towards Tackling Capacity-Bound Models Using DRAMs Over SRAMs," 2024 IEEE 21st India Council International Conference (INDICON), Kharagpur, India, 2024, pp. 1-6, doi: 10.1109/INDICON63790.2024.10958400.
[14] IEA (2025), Global data centre electricity consumption by sensitivity case, 2020-2035, IEA, Paris https://www.iea.org/data-and-statistics/charts/global-data-centre-electricity-consumption-by-sensitivity-case-2020-2035, Licence: CC BY 4.0
[15] Micron Technology, Inc, 4Gb DDR3 SDRAM Component Data Sheet: MT41J512M8, 2009.
[16] A. Ben Abdallah and K. N. Dang, Neuromorphic Computing Principles and Organization, 2nd ed., Springer, 2025, ISBN: 978-3-031-83091-4.
[17] Y. Hanyu and K. N. Dang, "EnsembleSTDP: Distributed in-situ Spike Timing Dependent Plasticity Learning in Spiking Neural Networks," 2024 IEEE 17th International Symposium on Embedded Multicore/Many-core Systems-on-Chip (MCSoC), pp. 434-440, 2024.

## Slide 35: Thank you for your attention!

## Slide 36: Details
The DRAM cell is implemented using HSPICE
Capacitance: 25 fF, Refreshing frequency: 15.625 Hz
Monte Carlo simulation is performed with Gaussian Variation on voltage
Temperature is varied and its relation to the error percentage is found
Ran training and testing of Neural Network, identified fault insertion parameters and location
Faults have been inserted during training

## Slide 37: Rate Coding
Converts raw sensor data into spike trains and processed by an SNN
High pixel intensity = High spike frequency
Transmitting 1-bit spikes is more efficient
Spikes generated from MNIST image
Input = 1
Input = 0
Notes: Now that we have converted our heavy image data into lightweight binary spikes, how does the hardware actually process them